WIND RATING

We are occasionally asked what the wind rating is on our blinds.

This is a complex question that cannot be answered simply, because;

- The wind load on a blind is directly proportional to its area, so its ability to withstand winds depends on its size.

- The wind load on a conventional blind is transferred to the top tube and base bar, with a Slidetrack blind the wind load is transferred to its entire perimeter so can withstand up to twice the loading.

- The location of a blind within a given wind speed area is also very important, e.g. whether it is in an exposed or sheltered area, or on a window or a verandah.

However, we have thousands of blinds successfully installed in N1 (W28) and N2 (W33) wind rating areas throughout Australia and overseas, which is the best product testament possible. (These categories refer to potential gust wind speeds up to 28 and 33 m/sec respectively.)

We do recommend that blinds are retracted during storms, particularly larger blinds over 7.5 sq m.

Motorised blinds, particularly when wider than about 2m may require manual assistance when being lowered in windy conditions.

ooOoo